## Slide 1: Payroll System Cost Projection
Red Team: Sarah, Matt, Andrew, Aaron, Jimmy

## Slide 2: Supplied information/considerations
  Pay Rate: $25/hour/person
  4th Gen language 53 LOC/Function Point
  No longer printing checks in house
  $1500 for in house hardware

## Slide 3
FUNCTION POINT ESTIMATION |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | Weighting Factor |  |  |  |  | 
Measurement parameter |  |  | # simple | simple | #average | average | # complex | complex |  |  | 
# of user inputs |  |  | 4 | 3 | 0 | 4 | 0 | 6 | = | 12 | Employee#, Admin ID/pass, Barcode, button press
# of user outputs |  |  | 2 | 4 | 0 | 5 | 0 | 7 | = | 8 | Screen, file
# of user inquiries |  |  | 4 | 3 | 0 | 4 | 0 | 6 | = | 12 | clock in/clock out, admin features, time table,
# of files |  |  | 2 | 7 | 1 | 10 | 0 | 15 | = | 24 | employee table, time table, cheque file
# of external interfaces |  |  | 2 | 5 | 0 | 7 | 0 | 10 | = | 10 | User/admin,User IO
 |  |  |  |  |  |  |  | Count-total = |  | 66 | 
Rate each factor on a scale of 0 to 5: |  |  |  | 0 - No Influence |  | 1 - Incidental |  | 2 - Moderate |  |  | 
 |  |  |  | 3 - Average |  | 4 - Significant |  | 5 - Essential |  |  | 
1. Does the system require reliable backup and recovery? |  |  |  |  |  |  |  |  |  | 4 | yes, payroll, losing this is bad
2. Are data communications required? |  |  |  |  |  |  |  |  |  | 3 | yes, must talk to bank and offsite host
3. Are there distributed processing functions? |  |  |  |  |  |  |  |  |  | 0 | no
4. Is performance critical? |  |  |  |  |  |  |  |  |  | 5 | yes, payroll
5. Will the system run in an existing, heavily utilized operational environment? |  |  |  |  |  |  |  |  |  | 0 | no, new system
6. Does the system require on-line data entry? |  |  |  |  |  |  |  |  |  | 1 | Not exactly, backup once a day
7. Does the on-line data entry require the input transaction to be built over multiple screens or operations? |  |  |  |  |  |  |  |  |  | 1 | No, but this could change, so incidental for time being
8. Are the master files updated on-line? |  |  |  |  |  |  |  |  |  | 5 | yes, payroll
9. Are the inputs, outputs, files, or inquiries complex? |  |  |  |  |  |  |  |  |  | 0 | only if pushing buttons is considered hard
10. Is the internal processing complex? |  |  |  |  |  |  |  |  |  | 2 | no, storing data and basic arithmetic
11. Is the code designed to be reusable? |  |  |  |  |  |  |  |  |  | 5 | absolutely
12. Are conversion and installation included in the design? |  |  |  |  |  |  |  |  |  | 5 | yes, customer not tech savvy
13. Is the system designed for multiple installations in different organizations? |  |  |  |  |  |  |  |  |  | 5 | yes, considering future expansion
14. Is the application designed to facilitate change and ease of use by the user? |  |  |  |  |  |  |  |  |  | 5 | users not tech savvy, yes
 |  |  |  |  |  |  |  | sum of Fi = |  | 41 | 
 | Funtion Point Metric = |  |  | count-total * [.65+.01*sum Fi] |  |  |  |  |  |  | 
 |  |  |  | 70 |  |  |  | 0.95 | 62.7 |  | 
 | LINES OF CODE | 3710 |  |  |  |  |  |  |  |  | 

## Slide 4
Payroll System |  |  |  |  |  | 
Cost Estimation |  |  |  |  |  | 
team size: | 5 |  |  | LOC (est. per peson) |  | 
LOC/Month | 465 |  |  | Aaron | 80 | 
Program LOC | 3710 |  |  | Andrew | 110 | 
Worst Case(in months): | 7.97849462365591 |  |  | Matt | 90 | 
Best Case(in months) | 5.99461883119382 |  |  | Jimmy | 90 | 
Hours per week | 100 | 20 hrs/person |  | Sarah | 95 | 
weekly cost | 2500 |  |  |  |  | 
Monthly Cost | 10000 |  |  |  |  | 
Estimated Project Length | 8 | months including | testing & installation |  |  | 
Software Cost | 80000 | USD |  |  |  | 
Project cost | 81500 | USD |  |  |  |